## Slide 1: Providing Privacy, Safety, and Security in IoT-Based Transactive Energy Systems using Distributed Ledgers
in partnership with Siemens, CT
Abhishek Dubey Vanderbilt University | Aron Laszka University of Houston

## Slide 2: Electrical Energy Networks are Changing
From centralized to decentralized and distributed energy systems
Changing Generation Mix
Transactive Energy
Electric Cars
Decentralization
DER-s
Increasing Complexity

## Slide 3: Decentralization is the Big Trend

## Slide 4: The Evolution of Energy Networks
Traditional networks with transmission system operators, distribution system operators, and radial distribution systems to communities

## Slide 5: The Evolution of Energy Networks
Network of distribution feeders with some microgrids with tightly integrated distributed energy resources
Advantages of decentralization
  improved cyber and physical reliability by removing single point of failures
  faster decision making by avoiding network penalties due to round-trip to the cloud
  improved scalability
  better integration with hierarchical control systems

## Slide 6: The Evolution of Energy Networks
Trend
Network of transactive microgrids with limited role of distribution system operators
Network of distribution feeders with some microgrids with tightly integrated distributed energy resources
Traditional networks with transmission system operators, distribution system operators, and radial distribution systems to communities

## Slide 7: Trend of Decentralization
Trend
Network of transactive microgrids with limited role of distribution system operators
Network of distribution feeders with some microgrids with tightly integrated distributed energy resources
Traditional networks with transmission system operators, distribution system operators, and radial distribution systems to communities
This trend of decentralization can be seen around many other cyber-physical system applications, for example: smart manufacturing, smart cities, etc.

## Slide 8: Smart Homes with Production and Delayed Consumption Capability are the Key to this New Trend

## Slide 9: Smart Homes → Smart Prosumers
Energy Exchange
Reduces Dependence on the Grid
typical generation and consumption profile
Participant 1
Participant 2

## Slide 10: Transactive Energy
Requirements:
Local energy market safety and efficiency
  time synchronized distributed IoT platforms problem
Integrity and auditability of finalized transactions
  decentralized management problem
Information privacy for prosumers
  distributed protocol problem
Energy Exchange
Reduces Dependence on the Grid

## Slide 11: Focus Challenge: Privacy
Information privacy
  leakage of energy usage patterns to other prosumers
  inference of future states from prosumer transactions
  transactions and energy usage data in a transactive microgrid are much richer sources of information than the simple usage data collected by smart meters
Example: residents leave their house for the evening
1. smart home decides to sell surplus energy
2. smart home posts offer to sell energy future
3. other prosumers in the microgrid learn that the residents will not be home

## Slide 12: RIAPS: Our Baseline System Model
http://riaps.isis.vanderbilt.edu
programming model (for distributed real-time software) on embedded nodes dispersed throughout the power grid
services (for application management, fault tolerance, security, time synchronization, coordination, etc.)
PI: Gabor Karsai, Vanderbilt university, http://riaps.isis.vanderbilt.edu

## Slide 13: PETra Trading Platform and Distributed Ledger Architecture
We introduce PETra, a blockchain-based solution that enables consumers to trade energy without sacrificing their privacy and provides safety and security for the grid. It provides the following:
A RIAPS Node Participating in PETra-Enabled Transactive Energy Market
The node runs the necessary logic to participate in the trading

## Slide 14: PETra Trading Platform and Distributed Ledger Architecture
We introduce PETra, a blockchain-based solution that enables consumers to trade energy without sacrificing their privacy and provides safety and security for the grid. It provides the following:
PETra
Bid Storage
  by serving as a database for bids, enables prosumers to find trade partners without communicating with all potential partners

## Slide 15: PETra Trading Platform and Distributed Ledger Architecture
We introduce PETra, a blockchain-based solution that enables consumers to trade energy without sacrificing their privacy and provides safety and security for the grid. It provides the following:
PETra
Bid Storage
  by serving as a database for bids, enables prosumers to find trade partners without communicating with all potential partners
Distributed Ledger
  stores transactions that specify trades, energy production and consumption values, financial records, and regulatory policies for the microgrid

## Slide 16: PETra Trading Platform and Distributed Ledger Architecture
We introduce PETra, a blockchain-based solution that enables consumers to trade energy without sacrificing their privacy and provides safety and security for the grid. It provides the following:
PETra
Bid Storage
  by serving as a database for bids, enables prosumers to find trade partners without communicating with all potential partners
Controller (Future)
Distributed Ledger
  stores transactions that specify trades, energy production and consumption values, financial records, and regulatory policies for the microgrid
  stabilizes load within the microgrid and controls it based on the load in the rest of the grid

## Slide 17: PETra Trading Platform and Distributed Ledger Architecture
We introduce PETra, a blockchain-based solution that enables consumers to trade energy without sacrificing their privacy and provides safety and security for the grid. It provides the following:
PETra
Bid Storage
  by serving as a database for bids, enables prosumers to find trade partners without communicating with all potential partners
Controller (Future)
  stabilizes load within the microgrid and controls it based on the load in the rest of the grid
Distributed Ledger
  stores transactions that specify trades, energy production and consumption values, financial records, and regulatory policies for the microgrid
smart meters must be tamper resistant to prevent prosumers from “stealing electricity” by tampering with their meters
Smart Meters

## Slide 18: The PETRA Protocol

## Slide 19: Security Assumptions
Billing is performed by the tamper proof smart meters based on the energy prices set by the DSO, the energy trades recorded in the blockchain, and the energy transfer recorded by the smart meter
Regulatory policies are set by the DSO and cannot be changed by anyone else
Prosumers cannot back out of trades unilaterally, and they can be banned by the DSO

## Slide 20: Privacy Guarantees
Only the corresponding smart meter and the DSO may gain information regarding the amount of energy produced, consumed, bought, or sold by a prosumer
Only the prosumer may know which bids and asks it has posted, and no one can know who traded energy with whom

## Slide 21: Energy Assets: PETra Key Concept
Energy is traded as quantized assets during fixed time intervals:
  power: non-negative amount of power to be produced/consumed (for example, measured in watts)
  start: first time interval in which energy is to be produced/consumed
  end: last time interval in which energy is to be produced/consumed
A prosumer/consumer must withdraw assets from its smart meter before engaging in trading
  selling energy → production asset
  buying energy → consumption asset

## Slide 22: Energy Assets: PETra Key Concept
Other assets are financial, which are exchanged after settlement of a trade
All transactions are recorded in the distributed ledger
  auditable
  immutable

## Slide 23: Energy Assets: PETra Key Concept
Other assets are financial, which are exchanged after settlement of a trade
All transactions are recorded in the distributed ledger
  auditable
  immutable
Problem: all transactions in the distributed ledger are public and can be traced back to the account holder

## Slide 24: Anonymous Addresses
Transactions on Bitcoin and similar blockchains provide pseudo-anonymity
  each transaction is associated with the public addresses of the sender and receiver, which enables tracking trades
  anonymous addresses may be created
  however, these addresses can be easily linked to the prosumers’ public addresses as soon as they transfer assets to them

## Slide 25: Anonymous Addresses and Mixing Services
Mixing services such as Zerocoin and Xim use accumulators and Zero Knowledge Proofs to mix transactions from a number of addresses together and then record them on the blockchain
Due to this, it is not possible to identify the individual senders and link them to the anonymous addresses on the output
In PETra, we build on such a mixing service and use it to provide anonymity for trading
prosumer 1
prosumer 2
prosumer 3
mixing service
anonymous address 1
?
?
?
anonymous address 2
anonymous address 3

## Slide 26: Full Trading Workflow
Simplified overview of the flow of assets from the perspective of a prosumer who sells energy.
Note that to prevent de-anonymization, a prosumer should use multiple addresses and multiple rounds of mixing, which we have omitted from the figure for clarity of presentation.
DSO regulates using pricing and limiting asset withdrawals
Tracking anonymous energy assets enables enforcing safety requirements without violating prosumer privacy

## Slide 27: PETra Implementation 2.0 (DSO as Mixer)
DSO regulates using pricing and limiting asset withdrawals
Tracking anonymous energy assets enables enforcing safety requirements without violating prosumer privacy

## Slide 28: Evaluation (since the paper was written)
We used real-world energy production / consumption data from a German microgrid
We deployed our system on a private Ethereum network
90% of trades were closed within 23 seconds or less

## Slide 29: Summary
Energy Exchange
Reduces Dependence on the Grid
Information privacy
  energy assets, anonymous addresses, and mixing services
Assuring integrity and auditability of finalized transactions
  distributed ledger and tamper proof smart meters